## Slide 1: PIC &PPI
PPI Mode 2 with PIC(8259)

## Slide 2: OCW1

## Slide 3: OCW2

## Slide 4: OCW3

## Slide 5: INTA waveform

## Slide 6: Address Decoding for the Peripherals
8086
8255A
PPI
A0
A1
Latch (‘373)
Decoder
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
X0
X1
X2
A0
A1
A2
A3
A4
A5
A6
A7
CS
8259
A0
CS
AD0-AD7
D0-D7
Buffer
ALE
PPI Address: 011XXPP0
8259 Address: 101XXXP0
ACK_A
STB_A
IR0
IR1

## Slide 7: Port Addresses
PORTA EQU 01100000b
PORTB EQU 01100010b
PORTC EQU 01100100b
PPICOM EQU 01100110b
P8259_0 EQU 10100000b
P8259_1 EQU 10100010b
PPI Address: 011XXPP0
8259 Address: 101XXXP0

## Slide 8: PIC Initializing Sequences

## Slide 9: ICW1
  MOV AL , 00010011b ;Edge – Single – ICW4
  OUT P8259_0 , AL

## Slide 10: ICW2
  MOV AL , 80H ; Interrupt Type
  OUT P8259_1 , AL
Addresses would be: 80H to 87H

## Slide 11: ICW3
Master Mode
Slave Mode
Is not needed in Single Mode

## Slide 12: ICW4
  MOV AL , 00000001b ; 8086 CPU
  OUT P8259_1 , AL

## Slide 13: OCW1
  MOV AL , 11111100b ; Mask IR2 to IR7
  OUT P8259_1 , AL

## Slide 14: Initialize 8259
INIT_8259:
  MOV AL , 00010011b ;Edge – Single – ICW4
  OUT P8259_0 , AL
  MOV AL , 80H ; Interrupt Type
  OUT P8259_1 , AL
  MOV AL , 00000001b ; 8086 CPU
  OUT P8259_1 , AL
  MOV AL , 11111100b ; Mask IR2 to IR7
  OUT P8259_1 , AL
  RET

## Slide 15: Initializing PPI
INIT_PPI:
  MOV AL , 40H ;01XXXXXX Selecting Mode 2
  OUT PPICOM , AL
  MOV AL,1
  MOV [TX_FLAG] , AL ; Flag Indicating Empty Buffer
  XOR AL , AL
  MOV [RX_FLAG] , AL ; Flag Indicating Empty Buffer
  MOV [TX_head],AL
  MOV [RX_head],AL
  MOV [TX_tail],AL
  MOV [RX_tail],AL
  RET

## Slide 16: OCW2
MOV AL,01100000b ;OCW2 (EOI for IR0)
OUT P8259_0,AL

## Slide 17: Transmit Interrupt
INT_TX:
PUSH AX
PUSH BX
CALL TX_AVAIL_SIZE
JNZ CONT_TX
MOV AL,1
MOV [TX_FLAG],AL
JMP STOP_TX
CONT_TX:
MOV BX,TX_BUF
MOV BL,[TX_tail]
MOV AL,[BX]
OUT PORTA,AL
INC BL
MOV [TX_tail],BL
STOP_TX:
MOV AL,01100000b ;OCW2 (EOI for IR0)
OUT P8259_0,AL
POP BX
POP AX
IRET

## Slide 18: Receive Interrupt
INT_RX:
PUSH AX
PUSH BX
CALL RX_EMPTY_SIZE
JNZ CONT_RX
MOV AL,1
MOV [RX_FLAG]
  JMP STOP_RX
CONT-RX:
IN AL,PORTA
MOV BX,RX_BUF
MOV BL,[RX_head]
MOV [BX],AL
INC BL
MOV [RX_head],BL
STOP_RX:
MOV AL,01100001b ;OCW2 (EOI for IR1)
OUT P8259_0,AL
POP BX
POP AX
IRET

## Slide 19: Set Interrupt Vectors
MOV AX,CS
MOV BX,INT_TX
MOV [4*80H],BX
MOV [4*80H+2],AX
MOV BX,INT_RX
MOV [4*81H],BX
MOV [4*81H+2],AX
INT_TX:LOW
INT_TX:HIGH
CS:LOW
CS:HIGH
INT_RX:LOW
INT_RX:HIGH
CS:LOW
CS:HIGH
200H
201H
202H
203H
204H
205H
206H
207H

## Slide 20: Transmit Function
Transmit: ;Addr in SI, Size in CX
CALL TX_EMPTY_SIZE
JNZ CONT_Transmit
CALL Check_PPI_TX
CONT_Transmit:
MOV AL,[SI]
CALL PUTCHAR
INC SI
LOOP Transmit
CALL Check_PPI_TX
RET

## Slide 21: Checking PPI for Transmit
Check_PPI_TX:
MOV AL,[TX_FLAG] ;Check if PPI Empty for TX
AND AL,AL
RETZ
MOV AL,[TX_FLAG] ;Check again.
AND AL,AL
RETZ
CALL TX_AVAIL_SIZE
RETZ
MOV BX,TX_BUF
MOV BL,[TX_tail]
MOV AL,[BX]
OUT PORTA,AL
INC BL
MOV [TX_tail],BL
XOR AL,AL
MOV [TX_FLAG],AL
RET

## Slide 22: Receive Data
GETCH: ;Wait Until a char is received
CALL RX_AVAIL_SIZE
JNZ GETCHAR
CALL Check_PPI_RX
JMP GETCH

## Slide 23: Checking input Buffer
Check_PPI_RX:
MOV AL,[RX_FLAG] ;Check if PPI Empty for TX
AND AL,AL
RETZ
MOV AL,[RX_FLAG] ;Check again.
AND AL,AL
RETZ
CALL RX_EMPTY_SIZE
RETZ
IN AL,PORTA
MOV BX,RX_BUF
MOV BL,[RX_head]
MOV [BX],AL
INC BL
MOV [RX_head],BL
XOR AL,AL
MOV [RX_FLAG],AL
RET

## Slide 24: Data Storage Policy
Process
TX_FIFO
PPI
RX_FIFO
TX_Service
RX_Service
Transmit
Receive

## Slide 25: Initializing PPI
INIT_PPI:
  MOV AL , 40H ;01XXXXXX Selecting Mode 2
  OUT PPICOM , AL
  MOV AL,1
  MOV [TX_FLAG] , AL ; Flag Indicating Empty Buffer
  XOR AL , AL
  MOV [RX_FLAG] , AL ; Flag Indicating Empty Buffer
  MOV [TX_head],AL
  MOV [RX_head],AL
  MOV [TX_tail],AL
  MOV [RX_tail],AL
  RET

## Slide 26: Checking FIFO
TX_AVAIL_SIZE:
MOV AL,[TX_head]
MOV BL,[TX_tail]
SUB AL,BL
RET
TX_EMPTY_SIZE:
MOV AL,[TX_head]
MOV BL,[TX_tail]
SUB AL,BL
NOT AL
RET
RX_AVAIL_SIZE:
MOV AL,[RX_head]
MOV BL,[RX_tail]
SUB AL,BL
RET
RX_EMPTY_SIZE:
MOV AL,[RX_head]
MOV BL,[RX_tail]
SUB AL,BL
NOT AL
RET